## Slide 1: 802.1 af discussion
First two slides are my picture of ae requirements - these may need some refining
Next slide is my interpretation of KSP implementation of CA
then discovery with and without preshare CAK
Remaining slides talk about af requirements and issues
  Requirements for discovery
    A proposal for “device” authorization
  Issues with
    Race Conditions (and a security proposal)
    whether EAP and RADIUS are appropriate
This is meant to be a discussion support, not a specification
The discussion might be best broken into
a)initialization - slide 1- 13, and
b) AS/backend issues slide 10-16 (overlap provides a segway)

## Slide 2
A
B
D
C
CAabcd
SCA
SCB
CA = Secure Connection Association
SCi = Secure Channel from Station (I) to all stations on CA
SAij = Security Association Station (i) to Station (j)
SAKij = Secure Association Key instance (i) for Station (j)
SCC
SCD

## Slide 3
KaYi = Key Agreement Entity - one or more at each Station
SecYi = Security Entity - one (or more?) at each Station
Announcement = Procedure by which KaY announces its presence and desire to join a CA
Discovery = Procedure by which KaY discovers other KaYs participating in or attempting to join a CA
A
B
D
C
CAabcd
SecYA Internal DB
SAAB - [SAKB]
SAAC [SAKC]
SAAD [SAKD]
SAKA

## Slide 4
A
B
D
C
CA
KSP implementation of CA
CA defined by (has) common CA Key - CAK and Key Generating Key - KGK
All Stations generate the same SAK from the common KGK (and other info descrubed in Mick’s dicument) to protect transmit by all stations connected to the CA

## Slide 5
A
B
D
C
CA
CAK
KGK
KaY-A
SAKn
.
.
Connecting to CA requires setting
CAK and KGK -- could be hand configured or done with some initialization protocol

## Slide 6
A
B
D
C
CA
CAK=null
KGK=null
KaY-A
request connection
to CA
Respond to request on behalf of CA
establish dialog with KaY-A
Establishing CAK, KGK for station attempting to join CA

## Slide 7
A
B
D
C
CA
Connection dialog between A, asking for CAK and KGK for CA and
D which is already in CA and which can give the CAK and KGK to A if it is satisfied with the conversation
Note: D is acting “for” CA. If it authoriizes A then A is authorized to join CA
?- what protection supports the connection between A and CA

## Slide 8: Functions for a KaY
Discover other KaY
IF Connecting - Authorize with CA through other KaYs
  Create SAij with (each?) KaY
    In KSP protoocl document only one SA is needed
Get/Generate CAK and KGK
Create SAK for itself and share with each authorized KaY using the SA for that KaY
Update SAK periodically
  use existing SAK to select the next (see KSP doc)

## Slide 9: Discovery- Generic
  These are assumptions for “generic” KaY-
  KSP simplifies these as shown on next slide
  Each Kay Periodically announces presence
    If KaY hears announcement it determines if it knows the announcing KaY
      If it sees a new KaY (to it) then it establishes an authorization dialog with it and attempts to create a SA
    If a KaY attempts to join a CA it announces its presence and all existing KaYs attempt to create and SA with it
    If two KaYs attempt to joint a CA each announces its presence. If a KaY attempting to join sees an announcement it attempts to authorize the announcer.
    It is possible that two (or more) KaYs may try to authorize each other. The authorization dialog must be able to detect and manage this

## Slide 10: Discovery- KSPc
  These are assumptions for KSP style KaY-
  KSP simplifies generic requirements
  Each Kay Periodically announces presence using CAK to protect / provide integrity
    If KaY hears announcement from another KaY knowing the CA
      It checks the Key Number and updates SAK if necessary
        see KSP document for details
  If a KaY attempts to join a CA but does not know the CA, the proper procedure does not yet seem defined.
    Possible approach is
      Announce its presence to all KaYs currently joined to CA
      One of connected CAs responds and authorizes the supplicant KaY
      Supplicant and respondent have authorization dialog
      If respondent is satisfied it gives the Supplicant the CAK and KGK

## Slide 11: Authorization
description of af seems to be functionally very similar to key exchange for 11i
As with 11i, af does not define protocol for getting the common key that lets stations know each other
  af needs CAK and KGK, 11i needs Master Key
  neither describes a specific authorization protocol
  11i does define use of 1.X and EAP as protocol for authorization
  1.X defines controlled/uncontrolled port as way of controlling data while in authorization mode

## Slide 12: Authorization Protocol
This protocol that allows a KaY to authenticate and get CAK and KGK
  not needed if CAK/KGK is hand configured in KaY
Requires a conversation that does not have a CAK
  some ability for DOS attacks during anu unprotected part of this conversation

## Slide 13: Announcements
A KaY attempting to join a CA announces itself
  The announcement is on a Connectivity Association which allows stations to talk
Announcement includes a System and port id (? I think this is right)
Announcement (may?) include a CA identifier
  to describe the CA it wants to join
Announcement is open to DOS since no SA exists
Announcement initiates Authorization Dialog(s)

## Slide 14: Announcement (initialization proposal)
To limit the DOS possibilities of sending unknown Announcements it is proposed to *allow* KaY to use asymetric key to “sign” Announcement
Announcer sends public key with announcement signed by private Key
Receiver verifies the signature using the included public key
  , creates symmetric key for authorization dialog
  signs reply (including symmetric key) with public key,
Symetric key is not used to protect Authorization dialog
  this avoids DOS attacks that disrupt the conversation
  authorization is of a KaY known to have received the symetric key.
If authorization dialog succeeds CAK/KGK can be sent to the proposer

## Slide 15: Authorization (and Authentication) dialog requirements
Two KaYs attempting to create a SA between themselves will have an “authorization” dialog between themselves
  if included the initialization dialog is part of this
The authorization dialog will be done using some protocol between stations.
  EAP has been used in 1.X but seems to have some problems here
Each station may use a backend Authorization Server to support all or part of the dialog
Authorization Dialog will often include authentication dialog

## Slide 16: Authorization dialog race conditions
KaY may be set to support a single authentication or require dialog in both directions
  I.e. the CA may want to authenticate and authorize the applicant and the applicant may want to authenticate and authorize the CA
If single dialog is required to do mutual authentication, and it is possible that two KaY simultaneously initiate an applicant dialog, one will send a special response that indicates that it is terminating the method
  One KaY will then act as the “applicant” and the other as the “CA” in further dialogs

## Slide 17: Authorization entities
KaYi
KaYj
AS
AS
Connectivity Association
(e.g. Ethernet)
IP connection
IP connection

## Slide 18: Possible Authorization Sessions
KaYi
KaYj
ASi
ASi
Possible Dialogs
Kay-KaY - create “provisional” SA using assigned or created PK
- use pSA to have initial conversation
Either or both KaYs may decide to use a backend AS to get information requested by the other KaY
Either or both KaYs may request a backend to have a conversation with the other KaY (or its backend)
Each KaY will (presumably) control whether conversation is done by KaY or by a particular backend
? - is an AS acting for KaY (AS is “helper” for the KaY) --or is KaY controlling dialog and using one or more AS (note that in this example it does have an initial KaY-KaY cpmversatopm before anything else happens

## Slide 19
Authorization Dialog(s)
KaYi
KaYj
AS
AS
KaY to Jay
AS to AS
Dialog between KaYs may include initial (device) authentication and creation of authorization dialog key
EAP Dialog between ASs is typically an EAP method

## Slide 20: Examining RADIUS and EAP as KaY/AS communication
KaYi
KaYj
AS
AS
Radius Req
Radius Resp EAP Request
EAP Request
Radius Req EAP Request
This is non-standard and is not possible with existing standards
examining the possibility

## Slide 21: Other Radius/EAP Issues in dual AS architecture
RADIUS typically carries assertions from AS to NAS, based on results of EAP method
  This could work with KaYs in dual AS mode, allowing each AS to send assertions to its KaY as a result of EAP method
Protected Mode EAP methods may use “TLV”s within EAP method to signal from an AS to “peer” talking to NAS
  TLV to peer would go to remote AS and information in TLV sent via RADIUS Response to the KaY

## Slide 22: RADIUS/ EAP Changes
Initial EAP method request from KaYi to a KaYj would be translated at Kayi to RADIUS Request carrying an EAP Request.
  This is not possible now, but is a plausible possibility. It is not clear if this is a good idea for RADIUS.
EAP method for “peer” KaY would need to work on AS. This includes EAP checking for proper authentication as well as returning appropriate attributes to the “peer” KaY
This seems a lot of work in EAP - not clear how possible this might be?

## Slide 23: Getting the CAK/KGK
KaYs use initial key to support a “provisional” SA to protect data during the Initialization/Authorization step
uncontrolled port on KaY routes to AS
IP is used on uncontrolled ports to talk betwen KaYs and let KaYs forward to AS if appropriate
  each KaYs may routes to a different AS,
AS and KaY have a preestablished Security Association
Conversation might use WS protool or EAP/IP (PANA)
  Seems plausible alternative to RADIUS/EAP