## Slide 1: Semtech Wireless Products

## Slide 2: Standardization and a strong ecosystem are key to enable IoT
  LoRa™ Alliance Status:
    More than 90 members in LoRa Alliance, including industry leaders
      Cisco, IBM, Microchip, SK Telecom, Bouygues Telecom, Swisscom, Semtech, etc
    Members engaged with more than 50 MNO and major utilities
    Deployments: US, France, South Africa, Switzerland, Netherlands, Russia, Belgium, and China
    Module BOM cost $2-5
    More than 100 LoRaWAN products available
    Roadmap – low cost localization
Global Mobility
  LoRa™ Network Features:
  LoRaWAN™ Differentiation & Benefits
Security
True Location
Bidirectional
Multi-Usage
Low Cost
Max Lifetime
Long Range

## Slide 3: IoT Segments
Connected Devices by 2020 (billions)
* 50B Connected Devices in 2020
*
IoT Projected Volumes

## Slide 4
IoT Segment Trade-offs
Short Range
Communicating Devices
Long Range w/ Battery
Internet of Objects
Long Range w/Power
Traditional M2M
35% SOM
55% SOM
10% SOM
Well established standards
Good for:
  Mobile devices
  In-home
  Short range
Not good:
  Battery life
  Long range
Well established standards
Good for:
  Long range
  High data-rate
  Coverage
Not good:
  Battery life
  Cost
Emerging PHY solutions
Good for:
  Long range
  Long battery
  Low cost
  Positioning
Not good:
  High data-rate
Cellular
LPWAN
LAN

## Slide 5: IoT: Private vs Public Network
Private network – individually managed networks
  Individual network – Metering, security, home automation, industrial control
Public network – Telecom/operator managed networks
  Includes traditional private networks and permits numerous new applications
  A much more scalable model
Public
Network
Private
Network

## Slide 6
Motor bikes
Cars
Bicycles
Kids
Pets
Insurance – valuable assets
Find My Stuff
Forest fires
Air pollution
Earthquake sensors
Avalanche and flooding
Heating and AC
Equipment status
Factory control
SMART ENVIRONMENT & INDUSTRIAL
SMART CITY
SMART METERING
Irrigation control
Environment sensing
Animal tracking
Animal sensing – ovulation, birth
SECURITY/ SMART HOME
TRACKING
AGRICULTURE
Smart parking
Traffic sensors & control
Street lighting
Infrastructure monitoring
Trash and waste containers
Public events –location services
Advertising displays
Electric
Water
Gas
Infrastructure & production
Smoke detectors
Security systems
Smart appliances
Heating control / monitoring
LPWAN Applications

## Slide 7: Nationwide Networks Deploying
  Applications are many:
  Metering
  Supply chain management
  Maintenance / Supervision
  Alerting
  Identification / géolocalisation
  Back up for GSM existing solutions
Public Annoucements of Deployments by:
Fastnet (Telkom South Africa)
KPN (Holland)
Proximus (Belgacom) (Belgium)
Swisscom (Switzerland)
Bouygues (France)
Senet (USA)
Lace (Russia)

## Slide 8
Long Range Node IC
Long Range Gateway IC
What is LoRa?
Range >cellular at fraction of power
= 5-10 year battery life
= 5x lower sensor cost than cellular
LoRa
LoRaWAN
PHY
MAC Protocol
App
Application

## Slide 9: LoRa™ Network Features
Low Cost
  Minimal infrastructure
  Low cost end-node
  Open SW
Long Range
  Greater than cellular
  Deep indoor coverage
  Star topology
Max Lifetime
  Low power optimized
  10-20yr lifetime
  >10x vs cellular M2M
Multi-Usage
  High capacity
  Multi-tenant
  Public network

## Slide 10: LoRaWAN Differentiation and Benefits
True Location
  In/out door
  Accurate
Bidirectional
  Bidirectional
  Scalable Capacity
  Broadcast
Global Mobility
  True Mobility
  Seamless
  Roaming
Security
  Unique ID
  Application
  Network
www.LoRa-Alliance.org

## Slide 11: LoRaWAN System
Long range star network (same architecture as cellular)
  Easy to deploy/maintain, reduces cost of infrastructure, optimizes battery lifetime
Public or Multi-tenant networks managed by major telecom companies
  Enables customers to focus on end-node design/application not network management
  Reduces costs and complexity for all segments of the market

## Slide 12: LoRaWAN Segments and Ecosystem
Transceiver
Network Server
Application Server
SX127X family
Sensors
Modules
Base station
SX1301
Public Network Operator
Private Network Operator

## Slide 13: LoRa Range and Coverage
Coverage map from a single gateway/concentrator
  Cisco Webex building in San Jose
>30miles from San Jose to San Bruno

## Slide 14: Senet Silicon Valley Network
Three Senet towers deployed in Silicon Valley
Coverage map from three Senet towers (Joe’s drive home)
Tower 1:
Clay St, SFO
Tower: 2
Skeggs Peak
Tower 3:
North 1st, SJC

## Slide 15
LoRa Mote
FedEx Experiment:
LoRa for LP WAN Asset Tracking
LoRa Mote is dropped off / joins network
4/21/15 (5:00 pm)
Fed Ex Office: 454 El Camino Real, Redwood City CA

## Slide 16
Tower 1:
1st Street SJC
Tower: 2
Skeggs Peak
Tower 3:
Clay Street SFO
Data Rate=17 Temp =75F Battery =94%
LoRa Mote departs on truck
4/21/15 (7:10 pm)
Fed Ex Office: 454 El Camino Real, Redwood City CA
LoRa Mote
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 17
LoRa Mote
Driver goes to Port of Redwood City
4/21/15 (7:57 pm)
Nearest Tower: 9 Miles / Skeggs Peak
Data Rate=16 Temp= 75.2F Battery =92%
El Camino Real
Port of Redwood City
75.20
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 18
LoRa Mote
Driver goes to Menlo Park sorting facility
4/21/15 (8:03 pm)
Nearest Tower: 8 Miles / Skeggs Peak
Data Rate=16 Temp= 69.8F Battery =92%
69.80
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 19
Data Rate=16 Temp= 75.2F Battery =90%
LoRa Mote
Package spends the night at Oakland Airport on tarmac
4/21/15 (10:37 pm)
Nearest Tower: 11.4 Miles / Clay & Joes St SFO)
75.20
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 20
LoRa Mote
Package shows up at SJC sorting facility
4/22/15 (6:30 am)
Nearest Tower: 2.63 Miles / 675 North 1st Street SJC
66.20
Data Rate=16 Temp= 66.2F Battery =86%
4/22/15 (7:47 am)
Package moves across
warehouse
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 21
Package accidentally remains on truck in “outgoing” bin
Driver alerted 
LoRa Mote
Driver arrives at FedEx drop box
4/22/15 (10:00 am)
Nearest Tower: 2.60 Miles / 675 North 1st Street SJC
2nd Tower reports: 21.0 Miles / Skeggs Peak!
FedEx Experiment:
LoRa for LP WAN Asset Tracking

## Slide 22
LoRa utilized a spread spectrum based modulation
Advantages
Demodulate below noise floor – 30dB better than FSK
Better sensitivity than FSK (better Eb/No)
More robust to interference, noise, and jamming
Spreading codes orthogonal – multiple signals can occupy the channel
Tolerant to frequency offsets (unlike DSSS)
LoRa Modulation Overview

## Slide 23: LoRa Parameters and Interference Immunity
Parameter | Range | Effect | Change (125kHz)
Spreading Factor (SF) | 7-12 | DR | 300bps – 9.6kbps
 |  | Sensitivity | -138dBm to -121dBm
Bandwidth (BW) | 125K typ 10-500kHz | DR vs sensitivity | 300bps – 22kbps
Error correction | 4/5 to 4/8 | DR, time on air | 
Freq | 138M-1GHz |  | Frequency agnostic
Interfere | LoRa Co-Channel | FSK Co-channel
CW/FSK/GFSK | -5 to -20 | +8 to +10
Noise
Level
FSK
LoRa

## Slide 24: LoRaWAN Device Classes
Downlink Network Communication Latency
Battery Lifetime
Battery powered sensors
Most energy efficient
Must be supported by all devices
Downlink available only after sensor TX
A
Battery powered actuators
Energy efficient w/ latency controlled downlink
Slotted communication synchronized with a beacon
B
Mains powered actuators
Devices which can afford to listen continuously
No latency for downlink communication
C

## Slide 25: Bidirectional communication, class A
Receiver Initiated Transmission strategy (RIT)
End Device
Base station
Packet
Received by all base stations in range
End device sleeps
Rx slot 1
Rx slot 2
Cloud MAC Controller selects best base station

## Slide 26: Bidirectional communication, class B
Coordinated Sampled Listening (CSL) : Network may send downlink packet to node at any Rx slot
End Device
Base station
Received by all base stations in range
128 seconds
Rx1
Cloud MAC Controller selects best base station
BEACON
BEACON
Rx
2
Rx
3
Rx
4
Rx
5
Rx
x
Rx
x
Rx
x
Rx1
Rx1
Rx1
Rx1
Rx1
Rx1
Rx1
Rx1

## Slide 27: Adaptive Data Rate (ADR) 2D case, flat landscape
Energy / Time on air
Bitrate
SF12
11
10
9
8
7
14km
10km
8km
6km
4km
290bps
530
970
Avg bitrate ~1300bps
2D simulation (flat environment)

## Slide 28: Network Capacity Optimization
S6
S5
S1
S6
S4
S6
S2
G1
G2
LoRa Adaptive Data-Rate
Optimizes channel usage
Enlarges G1 capacity
Saves battery
S3
S5
S1
S2
S5
S6
Let free G1 capacity
(deep indoor)
(outdoor)
(outdoor)
(indoor)
(outdoor)
(deep indoor)
(indoor)
More capacity : New end-points
available on G1

## Slide 29: Current LoRaWAN Spec for North Amer.
Currently fixed channel plan with
  64 channels at 125 KHz uplink
  8 channels at 500 KHz uplink
  8 channels at 500 KHz downlink
Data rates for 125 KHz channels are SF7 to SF10
Maximum conducted power for uplink is 1W

## Slide 30: Wrap Up and Next Steps
LoRaTM enables the Internet of Things
Disruptive technology for IoT and tracking of assets
Provides outdoor and deep indoor connectivity
Very low cost of ownership with private or nationwide network deployments
Scalable architecture makes it future proof for capacity and interference
Strong ecosystem of partners and applications