## Slide 1: LoRaWAN Sensor Example
23-July-2015

## Slide 2: Goals
Demonstrate how to connect to Senet LoRaWAN network.
Send data via Senet network to IoT data storage M2X
Implement a If-This-Then-That (IFTT) trigger to send a response from M2X to the device (mDot)
Receive and process data at the device (mDot)

## Slide 3: LoRaWAN Uplink information flow
LoRaWAN
Gateway
LoRaWAN Device pre-programmed with ID and Routing Parameters.
DevEUI = Device ID, e.g. SSN AppEUI = Application ID, e.g. Employer AppKey = Encryption Key, e.g. ID Badge
Network Server
Application Server
Senet Co.
Check Device ID
Msg MIC Check
Duplicate Filter
Decode Packet
Fwd to App Owner
Data Storage
Visualization
IFTT Trigger
M2X

## Slide 4: LoRaWAN Downlink information flow
LoRaWAN
Gateway
LoRaWAN Device
Already JOINED
Network Server
Application Server
Senet Co.
Choose Tower
Queue Msg at Tower
Encrypt Packet
Queue Packet
IFTT Trigger calls
Senet URL
M2X

## Slide 5: Confirm Senet Account
Skip ahead only if you have completed setting up your Senet Account

## Slide 6: LoRaWAN Developer Portal
Developer login
Manage test devices
Transaction visibility
  PDU
  RF Attributes
Transaction forwarding
  Raw JSON
  ATT M2X
Initiate downlink communications
Export to CVS
http://app.senetco.com/senetdev

## Slide 7: Senet Developer Portal – Login Page
Begin registration process

## Slide 8: Senet Developer Portal – User Registration
Complete registration process

## Slide 9: Senet Developer Portal – New Device Registration
Register a new device
Device EUI from mDot sticker

## Slide 10: Senet Developer Portal – Device Detail
Set Data Range (display and export)
Export to CSV
Send Downlink
Configure Device

## Slide 11: Resume mDot Lab

## Slide 12: Import the Reference Project
From the following link import the project into your mbed workspace.
  https://developer.mbed.org/teams/Semtech/code/MTDOT_Senet_Demo_23-July
This project implements a simply tilt detector that can be used to report the Open or Close status of a garage door or mail box door.

## Slide 13: Update the project for your mDot
Update the AppKey on line #101 of main.cpp with the AppKey provided by Senet.

## Slide 14: Compile and Download your code
If we have updated everything correctly the project should compile without Error.
Make certain that you have the Virtual Comm Port active.
  Baud rate is 921600
Download the code to your mDot. (Drag to Multitech drive.)
You should see some messages indicating that your device has successfully connected to the Senet Network
  It is normal for the device to fail to ‘Join’ once or twice.

## Slide 15: Logging Data
Change the Orientation of your device.
Observe the data being saved on the Senet Developer Site.
  0001 == Flat
  0002 == Vertical

## Slide 16: Confirm M2X Account
Skip ahead only if you have completed setting up your M2X account

## Slide 17: M2X Sign-Up
Goto:
  https://m2x.att.com/signup
Sign up by using other accounts or enter the required fields
Select “SIGN UP” at the bottom of the page
If you use email you will need to confirm by following the link provided in the M2X activation email.

## Slide 18: M2X Account Activated
When your account is activated you should see a web page that allows you to create a new device.

## Slide 19: Create your device
Create your first device as shown to the right.
When done entering the fields select “Create” at the bottom of the page.

## Slide 20: Create a stream for your data
Start by selecting “Add Stream” as shown below.

## Slide 21: Add stream information
Add a unique stream ID. Use, “UpDown” as shown below.
Add a convenient Display Name. Perhaps “Door Status”.
Click “Save” to create and save this stream.

## Slide 22: Resume mDot Lab

## Slide 23: Forward to M2X from Senet Account
Login to Senet account and select the node.
Select the EUI Setup button (paper with pen icon)
Enter a description and select “Forward to M2X”
Copy from the M2X account the Primary API key
Copy from M2X the Device ID
Enter the stream ID of “UpDown”
4
2
3
5
6
5
4

## Slide 24: Logging Data at M2X
Change the Orientation of your device.
Observe the data being saved on the M2X Site.
  2 == Tilted Up
  1 == Flat

## Slide 25: Create a trigger (Turn on Light when Up)
From your M2X account create a trigger by selecting Triggers on the device page.

## Slide 26: Trigger Details (Light On when Up)
Enter the fields as shown to the right.
The Callback URL will enable M2X to send a message to your mDot.
The Callback URL details are on the following page.
Press “Save” after entering the customer Callback details.

## Slide 27: Callback URL
A Callback URL is required by the trigger to enable an action to take place when the condition specified by the trigger is satisfied.
In order to send a message to your mDot while connected to the Senet network the following URL is customized
  http://app.enertrac.com/senetdev/m2x.aspx?eui=[YourEUI]&port=1&user=[UserName]&value=0F
Replace [YourEUI] with the DevEUI (008000000000xxxx) of your mDot.
  (Do not include the “[“ or “]” in your URL.)
Replace [UserName] with your Senet account user name.
  (Do not include the “[“ or “]” in your URL.)
E.g.
http://app.enertrac.com/senetdev/m2x.aspx?eui=0080000000009C55&port=1&user=jknapp&value=0F

## Slide 28: Create 2nd Trigger (Off when down)
Create a second trigger using same fields but different
  Test condition
  Callback URL
Test Condition is “Equal to” == 1
Copy the previous Calback URL and change the value paramter to zero hex, 00
  http://app.enertrac.com/senetdev/m2x.aspx?eui=00250C0100000283&port=1&user=jknapp&value=00

## Slide 29: Put it all together
When the previous configuration is combined with the example UpDown mDot application a change in the condition of the mDot should be recorded by M2X and an appropriate message sent back to the mDot. The mDot receives the downlink data and turns its blue LED “On” or “Off”.